## Slide 1: Basic Use of Metrology Tools for QC Based on 3D Scanning and Point Clouds

## Slide 2: Contents
Key Concepts of Metrology
Quality Control Sensors and Software
Reference Architecture of the QC Solution
Basic Use of the Solution
Next Steps

## Slide 3: Key concepts of metrology

## Slide 4: What is Industrial Metrology?
The word “metrology” originated from two Greek words, “Metron” meaning measurement, and “Logos” meaning study. Metrology is the scientific study of measurement.
Each time products become more detailed and the limits of efficiency get pushed to new extremes, thus the manufacturing space has ever-tighter tolerances and precision to keep up.
It covers the calibration, maintenance, and quality control of measurement instruments and products used for industrial application and society in general, ensuring their suitability.
Proper measurement is critical in the industry as it affects the value and quality of the final product.
However, achieving this level of precision is only the first step; tolerances need to be measured and verified through metrology.
Metrology is important in all day-to-day tasks as it provides some quantitative information on the actual state of physical variables and processes.

## Slide 5: Some key concepts are…
Variation within a part's dimensions that is considered acceptable. A factor to consider is the manufacturing machine's ability to achieve these tolerances.
How close the average of a set of measured values is to the reference value, X. In manufacturing, this is the difference between the actual produced product and the CAD model or technical reference drawing.
How close each measurement is to the average of the measured values. Expressed statistically in terms of the standard deviation (𝜎). In metrology, the “standard” for standard deviation is ±2𝜎.
Expressions of precision and accuracy must also have an attached uncertainty value. This is the sum of the accuracy error and the precision error.

## Slide 6: Quality Control sensors and software
3D laser scanner and point clouds management SW

## Slide 7: Devices used for Dimensional Quality Control
Contact sensors
Non-contact sensors
Coordinate Measuring Machine
Measures the geometry of physical objects by sensing discrete points with a probe or optical sensor, that can move along three axes, X, Y and Z, orthogonal to each other in a three-dimensional Cartesian coordinate system. CMMs provide accuracy in the order of microns.
Versatile and flexible
Sub-micron level of accuracy
Long measuring time
Unsuitable for flexible or deformable components
Collects data from larger surface area in less time – high speed
Lower accuracy
Coverage of entire surface (not single measurement tracks)
Sensivity to surface characteristics
+ Metrology software

## Slide 8: 3D Laser Scanners
The one used for OPTIMAI Project (Microchip parts)
Generally use semiconductor lasers characterized by a red colored beam.
Digitization begins with the emission of a rectilinear laser beam which deforms on contact with the object.
Through the camera, the 3D scanner analyzes the deformation of the line emitted by the laser on the reliefs of the object in order to determine, by means of trigonometric calculations, its position in space.
Laser triangulation 3D scanners

## Slide 9: Metrology Software
Capture the reality – actual parts digitization
Scan the part and capture its point clouds, obtaining a virtual part, a very precise digital copy with high fidelity representation of the surfaces to allow automatic dimensional analysis.

## Slide 10
Reference arquitecture of the QC solution
Sensor + software package (inputs & outputs)

## Slide 11: Workflow of the Solution 3D Scanner + M3 Software
Physical part
CAD model
Raw point cloud processing
Pointcloud digital copy
Comparison of point clouds digital copy with CAD model
Disparity map
Results data in different formats as needed:
pdf report, stl with annotations, XML QIF file
Optiscan
M3 software
See module related to QIF standard*
CMM

## Slide 12: Work applied to Microsemi parts
Physical part
Raw point cloud processing
Pointcloud digital copy
Measurement analysis
Optiscan
M3 software
CMM
MTCL encapsulated PCBs and wafers
3D laser scanner

## Slide 13: Basic Guide for the use of the Solution

## Slide 14: Principal Characteristics of M3
MULTISENSOR
MULTIMACHINE
+ Intuitive software user interface

## Slide 15: Workflow in M3 Software - General Steps
Upload the CAD file of the part to the software
Create a measurement plan based on a STEP file (preparation of all needed geometries required to perform the measurement in the machine)
Perform the alignments (as part of the measurement plan)
Prepare the geometric tolerances needed for the validation of the part
Run the measurement program (with an optical sensor in this case)
Connect to the machine and execute the programs that measure the geometries in the part
Generate the results visualization in the software, by selecting any of the geometries that have been measured
2 options for this visualization: Create a report or visualize a color deviation mapping image for a comparison between CAD design and the actual measured part.
Export results in different formats: QIF, DMO, CSV, STEP IGS

## Slide 16: Next Steps

## Slide 17: Next Steps
Additional information can be found at
  https://www.innovalia-metrology.com/
  https://www.unimetrik.es/

## Slide 18: Thank you